## Slide 1: A Symbolic Analysis of Relay and Switching Circuits
1
2
3
4
5
6
A
B
C
D
SHEET
01
DRAWN SAMPLE DATE 1937-08-10 NTS
PROJECT
Shannon 1937 · Mock Defense
Sample defense · Shannon's 1937 master's thesis
A Symbolic Analysis of
Relay and Switching Circuits
Master's thesis, MIT, submitted August 10, 1937
Presenter: Sample Original author: Claude Shannon, MIT
W
X
Y
Z
S′
V
a
b
Xab = W + X + Y + ZS′V
W
X
Y
ZS′V
Fig. 6 (1938 paper): a network and its hindrance function
The dimension line carries algebra, not a length
Notes: Good morning, members of the committee. This is a sample thesis defense, using a real classic to show how a defense is put together: Claude Shannon's master's thesis, A Symbolic Analysis of Relay and Switching Circuits, submitted to MIT's Department of Electrical Engineering in 1937. I am not Shannon; the presenter field just says Sample. The drawing on the right is a real circuit from the paper, and the dimension line above it gives not a length but its algebra. That is exactly what this thesis is about.

## Slide 2: This defense in 16 sheets
1
2
3
4
5
6
A
B
C
D
SHEET
02
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Drawing index · Thesis record
This defense in 16 sheets
03 Background: how relay circuits were designed
04 Research question
05 Related work
06 Method: series is plus, parallel is times
07 Method: postulates and duality
08 Key derivation: simplifying Figure 5
09 Before and after: 13 contacts become 6
10 Applications in the thesis
11 Results and contributions
12 Limitations and influence
13 Conclusion
14 Acknowledgments
15 Backup A: notation and priority
16 Backup B: minimality and timing
Thesis record
Title
A Symbolic Analysis of Relay and Switching Circuits
Author
Claude Elwood Shannon
Dept.
Department of Electrical Engineering, MIT
Date
August 10, 1937 (date on the title page)
Degree
Master of Science, 1940
Advisor
Professor Frank L. Hitchcock
Paper
Condensed in Transactions of the AIEE, vol. 57, no. 12 (1938), pp. 713–723
Sources: thesis title page (MIT DSpace 1721.1/11173); AIEE Transactions 57(12):713–723 (1938). Click any row of the index to jump to that sheet.
Notes: First, the record. The thesis was submitted through the Department of Electrical Engineering on August 10, 1937, and the Master of Science was awarded in 1940, under the supervision of Professor F. L. Hitchcock. A condensed version appeared in 1938 in the Transactions of the American Institute of Electrical Engineers. On the left is the drawing index for this defense: every page that follows is a numbered sheet, with the sheet number in the title block at bottom right.

## Slide 3: Relay design was cut and try: slow, and seldom minimal
1
2
3
4
5
6
A
B
C
D
SHEET
03
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Background · the 1930s
Relay design was cut and try: slow, and seldom minimal
Detail A One coil drives two kinds of contact
X
X
X′
1
2
3
1
Coil: when energized, it moves all its contacts
2
Make contact X: closes when the coil operates
3
Break contact X′: opens when the coil operates
01
Where they were used
Automatic telephone exchanges, industrial motor controls, and almost any circuit built to carry out complex operations automatically.
02
Analysis: circuit → behavior
List every initial state of the switches and relays, then trace the chain of operations. In Shannon's words: “very tedious and open to frequent error”.
03
Synthesis: requirements → circuit
By “cut and try”: meet one requirement, then keep adding. The result is “seldom the simplest”, slow to reach, and often hides “sneak circuits”
Sources: Shannon's thesis, Chapter I, Introduction (pp. 1–2), quoted in the original wording; contacts have only two states, closed and open, per Section II of the AIEE paper.
Notes: Some background. Relay networks like these ran automatic telephone exchanges and industrial motor controls. The thesis opens with two problems. Analysis: given a circuit, find its behavior. The only way was to list every switch state and trace the chain of operations, which Shannon calls very tedious and open to frequent error. Synthesis: given the requirements, design the circuit. That meant cut and try, meeting one requirement and then adding the next, and the result was seldom the simplest and often hid sneak circuits. The detail on the left is a reminder: one coil drives both make and break contacts, and a contact has only two states, closed or open. That is the physical basis for all the algebra that follows.

## Slide 4: Research question: can algebra analyze, design and simplify switching circuits
1
2
3
4
5
6
A
B
C
D
SHEET
04
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Research question
Can switching circuits be written as equations and worked like algebra?
Q1
Analysis
Circuit → equations → behavior
See sheets 06–07
Q2
Synthesis
Specs → equations → circuit
See sheet 10
Q3
Simplification
Find the fewest contacts
generate equivalent circuits
See sheets 08–09
Sources: Shannon's thesis, Chapter I: “Two problems … analysis … synthesis”; AIEE paper, introduction: “methods of finding those particular circuits requiring the least number of relay contacts”.
Notes: So the thesis comes down to one question: can a switching circuit be written as equations and handled like an algebra problem? It breaks into three parts. Analysis: go from the circuit to equations. Synthesis: go from the requirements to equations, then draw the circuit straight from them. And simplification: find the circuit with the fewest contacts, and derive as many equivalent circuits as you like. Under each one is the sheet that answers it.

## Slide 5: Others came close; Shannon built a usable calculus
1
2
3
4
5
6
A
B
C
D
SHEET
05
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Related work
Others came close; Shannon built a usable calculus
1854
Boole
The Laws of Thought
1886
Peirce
A letter imagines logic done by switching circuits
1933
Huntington
Postulates for Boolean algebra (cited by Shannon)
1934–
Nakashima
A series of switching-theory papers in Japan
1935
Shestakov
A similar idea, published in 1941
1937
Shannon
A full circuit calculus
Top axis not to scale (NTS)
Three parallel lines of work (arrow: work continued after)
Nakashima
Papers from about 1934 onward
Shestakov
Proposed 1935, published 1941
Shannon
Thesis 1937, published 1938
1930
1935
1940
1945
Sources: Boole 1854 (Project Gutenberg #15114); Peirce's 1886 letter (historyofinformation.com #3634); Huntington, Trans. AMS 35 (1933), Shannon's reference (4); Nakashima and Shestakov per Wikipedia, James (2009) and the J. Symbolic Logic review index.
Notes: Here is the related work in order. The algebra was already there: Boole's Laws of Thought in 1854. In 1886 Peirce suggested in a letter that switching circuits could carry out logic. Shannon set his own circuit postulates beside Huntington's 1933 postulates for Boolean algebra to show they are equivalent. In the same years, Akira Nakashima at NEC in Japan published a series of papers on switching theory from about 1934, and Victor Shestakov in the Soviet Union proposed a similar idea in 1935 but did not publish it until 1941. Neither appears in the references of Shannon's 1938 paper. What sets Shannon apart is that he delivered a complete, workable calculus that engineers could design with directly.

## Slide 6: Series adds, parallel multiplies
1
2
3
4
5
6
A
B
C
D
SHEET
06
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Method · hindrance notation
Series adds, parallel multiplies
General note
One variable per contact, its “hindrance”:
X = 0
closed
X = 1
open
X
Y
a
b
X + Y
Series
Any contact open: the path is open
1 + 0 = 0 + 1 = 1
X
Y
a
b
XY
Parallel
Any contact closed: the path is closed
0 · 1 = 1 · 0 = 0
X′
a
b
X′
Break contact
Always the opposite of make contact X
X + X′ = 1, XX′ = 0
Each dimension line gives that circuit's hindrance function (Shannon's notation), not a length
Sources: AIEE paper, Section II, Fundamental Definitions and Postulates, Figs. 1–3, Postulates 1–4; the break contact is written X′, see Theorems 6a/6b.
Notes: This is the heart of the method. Shannon gives every contact a variable, its hindrance: 0 means closed, 1 means open. Put two contacts in series and the path is open if either one is open, so 1 plus 0 is 1: series is addition. Put them in parallel and the path is closed if either one is closed, so 0 times 1 is 0: parallel is multiplication. A break contact is written X prime, always the opposite of X. Look at the dimension line above each drawing: it measures not a length but the algebra of that circuit.

## Slide 7: Dual postulates, and a perfect match with logic
1
2
3
4
5
6
A
B
C
D
SHEET
07
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Method · postulates and duality
Dual postulates, and a perfect match with logic
Postulates 1–4 (columns a and b are duals)
Column a
Column b
1
0 · 0 = 0
1 + 1 = 1
2
1 + 0 = 0 + 1 = 1
0 · 1 = 1 · 0 = 0
3
0 + 0 = 0
1 · 1 = 1
4
At any time
X = 0
or
X = 1
Swap 0 and 1 and swap “·” and “+” in an a-equation to get its b-partner. As the paper stresses:
“It gives each theorem a dual theorem.”
Prove one theorem and you have proved its dual.
Table I Circuits vs. propositions (excerpt)
Symbol
Relay circuits
Propositions
X
The circuit X
The proposition X
0
Circuit closed
X is false
1
Circuit open
X is true
X + Y
X, Y in series
X or Y
XY
X, Y in parallel
X and Y
X′
Opposite of X
Not X
Sources: AIEE paper, Section II, Postulates 1–4 and the note on duality; Section II, Analogue with the Calculus of Propositions, Table I (excerpt, wording condensed).
Notes: These postulates come in pairs: swap 0 and 1, and swap times and plus, in column a and you get column b. Shannon stresses how much this matters: every theorem comes with a dual theorem, so proving one proves two. On the right is Table I from the paper. Read 0 as false and 1 as true, and series becomes OR, parallel becomes AND. The circuit calculus is an exact match for the propositional calculus, so every ready-made theorem of logic can be used directly to simplify circuits.

## Slide 8: Four steps of algebra simplify a tangled circuit
1
2
3
4
5
6
A
B
C
D
SHEET
08
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Key derivation · Figure 5
Four steps of algebra simplify a tangled circuit
Xab = W + W′(X + Y) + (X + Z)(S + W′ + Z)(Z′ + Y + S′V)
Start: hindrance function of Figure 5
= W + X + Y + (X + Z)(S + 1 + Z)(Z′ + Y + S′V)
17b with W as X: W′ → 1; 4a drops the 1 ·
= W + X + Y + Z(Z′ + S′V)
17b again with X, Y as X; 5a and 4a clear the brackets
= W + X + Y + ZZ′ + ZS′V
Distributive law 3a: multiply out
= W + X + Y + ZS′V
Theorem 6b: ZZ′ = 0; Theorem 4b: 0 + X = X
Theorem 17b
X + f(X, Y, Z, …) = X + f(0, Y, Z, …)
Sources: AIEE paper, Section II, Simplification example (Figs. 5 and 6) and Theorems 3a, 4b, 6b, 17b. All five lines appear on p.715; the paper names only Theorem 17b, the other theorem numbers are added here; first and last lines also checked equal by perfect induction (64 switch combinations).
Notes: This is the classic simplification example in the paper, done in four steps. We start from the hindrance function of the Figure 5 circuit. Step one uses Theorem 17b: when a variable is added to a function containing it, that variable can be set to 0 inside the function. Applied to W, W prime becomes 1. Step two applies the same theorem to X and then Y; since 1 plus anything is 1 and 1 times anything is itself, the whole bracket drops out. Step three multiplies out with the distributive law, and step four uses Z times Z prime equals 0, leaving W plus X plus Y plus Z S prime V. To be safe, I used Shannon's own method of proof, perfect induction, and checked all 64 combinations of the six switches: the first and last expressions agree every time.

## Slide 9: Same behavior, contacts cut from 13 to 6
1
2
3
4
5
6
A
B
C
D
SHEET
09
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Before and after · Figure 5 → Figure 6
Same behavior, contacts cut from 13 to 6
W
W′
X
Y
X
Z
S
W′
Z
Z′
Y
S′
V
a
b
W + W′(X + Y) + (X + Z)(S + W′ + Z)(Z′ + Y + S′V)
W
X
Y
Z
S′
V
a
b
W + X + Y + ZS′V
SIMPLIFY
Fig. 5 Before
Fig. 6 After
13 → 6
contacts
Sources: AIEE paper, Figs. 5 and 6; the paper notes: “Note the large reduction in the number of elements”. Contacts counted per p.715: each letter in an expression is one make or break contact; equivalence checked over all 64 switch combinations.
Notes: Draw the result of that derivation back as a circuit and you get this sheet. On the left, Figure 5: 13 contacts, nested three deep. On the right, Figure 6: just 6. The dimension line over each drawing is its own hindrance function. In the paper every letter stands for one contact, so counting letters counts contacts. The behavior is exactly the same. That is the value of algebraic simplification: pencil-and-paper work replaces rewiring a bench one lead at a time.

## Slide 10: Five examples; one circuit falls from 20 elements to 14
1
2
3
4
5
6
A
B
C
D
SHEET
10
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Applications · Section V
Five examples; one circuit falls from 20 elements to 14
Example 1 Selective circuit: U operates on 1, 3 or 4 of w, x, y, z
Synthesis:
U = S1,3,4(w, x, y, z)
→ draw Fig. 31
Elements, zero-based
Simplest series-parallel form (Fig. 30)
20
Symmetric-function method (Fig. 31)
15
Dual network of the negation (Fig. 33)
14
Fig. 33, in the paper's words: “This contains 14 elements and is probably the most economical circuit of any sort.”
Parts list · the other four examples
2
Electric combination lock
Five buttons a–e must be pressed in the order c, b, a and c together, d; a wrong press sounds an alarm.
3
Vote-counting circuit
12 voting switches and 13 lamps (0–12); pressing control button C lights the number of “yes” votes.
4
Binary adder
Switches hold the digits of two binary numbers; relays give each digit's sum and carry. The lowest sum digit is the exclusive OR of the two lowest digits.
5
Factor-table machine
Using the sieve of Eratosthenes, it prints the smallest factor of every integer up to 100 million and marks the primes.
Sources: AIEE paper, Section V, Illustrative Examples (selective circuit, lock, adder); vote counter and factor table in the thesis, Chapter V (pp. 58, 62). The examples are meant “to illustrate the use of the calculus in actual problems than to describe practical devices”.
Notes: Section V shows the method on five examples, and it answers the synthesis part of the research question: write the requirements as an equation, then draw the circuit directly. The selective circuit must operate U when exactly one, three or four of four relays operate. With a symmetric function that is one line: U equals S sub 1, 3, 4. Written as the simplest series-parallel form it takes 20 elements; the symmetric-function method brings it down to 15; and taking the dual network of its negation needs only 14. Shannon says this is probably the most economical circuit of any sort. The other four are an electric combination lock, a vote-counting circuit, a binary adder, and a machine that prints a factor table up to 100 million. One caveat: Shannon himself says these examples are there to illustrate the calculus, not to describe practical devices.

## Slide 11: Switching design became something you can calculate
1
2
3
4
5
6
A
B
C
D
SHEET
11
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Results and contributions
Switching design became something you can calculate
1
A calculus for circuits
Sheets 06–08
Every series-parallel circuit has a hindrance function; work it with the postulates and theorems to analyze, synthesize and simplify.
2
Circuits mirror logic
Sheet 07
The calculus is an exact analogue of the propositional calculus: any operation fully described in finitely many steps with “if”, “or”, “and” can be done automatically by relays.
3
A working toolkit
Sheets 08–10
Simplification theorems, non-series-parallel networks (star-mesh and delta-wye), symmetric functions, dual networks, and a binary adder.
How it was judged
Gardner: possibly the most important, most famous master's thesis of the century.
Howard Gardner; as quoted by MIT Slice and the MAA; paraphrased
Goldstine: it helped turn digital circuit design from an art into a science.
Goldstine, The Computer from Pascal to von Neumann, 1972, pp.119–120; as quoted; paraphrased
Prize
Alfred Noble Prize, 1939 (some sources say 1940)
Sources: Gardner via MIT Slice “Claude Shannon” and the MAA (original page not checked); Goldstine page numbers as cited on Wikipedia; 1939 Alfred Noble Prize per James (2009) (some sources give 1940).
Notes: I'd sum up the contributions in three points. First, a calculus for circuits: every circuit is a function, so design becomes calculation. Second, circuits mirror logic: in the paper's own words, any operation that can be completely described in a finite number of steps using if, or, and can be done automatically with relays. Third, a toolkit you can pick up and use: simplification theorems, star-mesh transforms, symmetric functions, dual networks and a binary adder. On the right are two attributed historical assessments. Howard Gardner called it possibly the most important, and also the most famous, master's thesis of the century; Herman Goldstine said it helped turn digital circuit design from an art into a science. The thesis also won the Alfred Noble Prize, awarded jointly by the American engineering societies, in 1939. Some sources say 1940; I follow the Royal Society memoir and use 1939.

## Slide 12: Sound method; mechanical minimization and timing came later
1
2
3
4
5
6
A
B
C
D
SHEET
12
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Limitations and influence
Sound method; mechanical minimization and timing came later
Limitations (mostly in the paper's own words)
What came next
How far simplification goes “depends somewhat on the ingenuity of the designer”: there is no mechanical procedure.
Original: “depends somewhat on the ingenuity of the designer”
Graphical methods: Veitch 1952, Karnaugh map 1953; tabular algorithms: Quine 1952, McCluskey 1956.
Minimality is guaranteed only among series-parallel forms; with arbitrary connections, only “in some cases”.
Original: simplest “containing only series and parallel connections”
Those methods minimize two-level AND-OR forms; minimizing general networks remains a separate problem.
Relays are assumed to act instantly, make and break contacts switching together; delays and sequence are add-ons.
Original: “This assumes that the relay operates instantly”
Systematic synthesis of sequential switching circuits: Huffman, J. Franklin Inst. 257 (1954).
Sources: AIEE paper, Sections I, II and IV (“ingenuity” in Section IV, p.721); Karnaugh, Trans. AIEE Pt. I 72(5) 1953; Quine, Amer. Math. Monthly 59(8) 1952; McCluskey, BSTJ 35(6) 1956; Veitch, Proc. ACM 1952, 127–133; Huffman, J. Franklin Inst. 257 (1954) 161–190, 275–303.
Notes: For the limitations, I've tried to use the paper's own words. First, how far simplification goes, the paper says, depends somewhat on the ingenuity of the designer; in other words, there is no mechanical procedure. Later, Veitch's and Karnaugh's graphical methods and the Quine–McCluskey tabular algorithm turned that step into a procedure. Second, minimality is guaranteed only for series-parallel circuits; with arbitrary connections a minimum can be found only in some cases. Third, it assumes relays act instantly and contacts switch together, with delays and sequencing handled as add-ons; a general theory of sequential synthesis had to wait for Huffman in 1954. Shannon also said himself that the examples in Section V are there to demonstrate the calculus, and that real designs must also respect constraints such as current capacity and the order in which contacts operate.

## Slide 13: Circuits are algebra, and algebra simplifies circuits
1
2
3
4
5
6
A
B
C
D
SHEET
13
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Conclusion
Circuits are algebra, and algebra simplifies circuits
W
X
Y
Z
S′
V
a
b
W + X + Y + ZS′V
1
2
3
1
Circuits can be written as algebra
Series is plus, parallel is times; hindrance 0 means closed, 1 means open. The expression on the dimension line is this drawing.
2
Algebra can simplify circuits
Figure 5's 13 contacts reduce to Figure 6's 6, with identical behavior across all 64 switch combinations.
3
Relays can do logic
The calculus mirrors propositional logic: break contact S′ is NOT, and series and parallel are OR and AND.
The drawing reproduces Figure 6 of the AIEE paper (see sheet 09); the mapping behind conclusion 3 is Table I (sheet 07).
Notes: To close, three sentences, all keyed to this drawing. One: circuits can be written as algebra; the expression on the dimension line is this circuit. Two: algebra can simplify circuits; Figure 5's 13 contacts become these 6, with the behavior unchanged. Three: relays can do logic; a break contact is NOT, series and parallel are OR and AND. That is where digital circuit design would later begin.

## Slide 14: Thank you. I welcome your questions.
1
2
3
4
5
6
A
B
C
D
SHEET
14
PROJECT
Shannon 1937 · Mock Defense
DRAWN SAMPLE DATE 1937-08-10 NTS
Thank you.
I welcome your questions.
This sample is drawn from Shannon's original text;
the thesis acknowledgments appear in the approval block below.
APPROVAL BLOCK
ADVISOR
Prof. F. L. Hitchcock (thesis acknowledgment page)
THANKS
Vannevar Bush · S. H. Caldwell (also thanked in the 1938 paper)
PRESENTER
Sample · not Shannon himself
Sources: thesis Acknowledgment page; AIEE paper, first-page footnote. The acknowledgments are from the original; the presenter is a placeholder.
Notes: That concludes my presentation. Thank you, and I welcome your questions and comments. The approval block below comes from the original acknowledgments: Shannon thanks his supervisor, Professor Hitchcock, and the 1938 paper also thanks Vannevar Bush and S. H. Caldwell.

## Slide 15: Backup Q&A: Why is series written as “plus”? / Did anyone get there first?
1
2
3
4
5
6
A
B
C
D
SHEET
15
PROJECT
Backup Sheets · Shannon 1937
DRAWN SAMPLE DATE 1937-08-10 NTS
Backup Q&A · A
Q
Why is series written as “plus”?
Shannon used hindrance: 0 is closed, 1 is open. In series, one open contact opens the path, so 1 + 0 = 1. Textbooks today use 1 for conducting, which makes series AND and parallel OR. The two notations are duals; Shannon's postulates come in pairs, so every theorem holds in both.
Source: AIEE paper, Section II, Postulates 1–4 and Table I.
X
Y
X + Y
X · Y
X
Y
XY
X + Y
Upper dimension = Shannon's hindrance (1 means open)
Lower dimension = today's conductance (1 means closed)
Q
Did anyone get there first?
Yes. Akira Nakashima at NEC published switching theory in Japan from about 1934; Victor Shestakov in the USSR proposed a similar idea in 1935, published in 1941. Shannon's 1938 paper cites neither. His contribution is a complete, workable design calculus.
Source: Wikipedia “Akira Nakashima”, “Victor Shestakov”; James (2009); AIEE references.
Nakashima
Papers from about 1934 onward
Shestakov
Proposed 1935, published 1941
Shannon
Thesis 1937, published 1938
1935
1940
← Back to sheet 6
← Back to contents
Notes: Backup sheet A. If the committee asks why the notation is the reverse of today's: Shannon used hindrance, 0 closed and 1 open, so series is plus; today we usually use conductance, so series is AND. The two are duals, and the postulates already come in pairs. If they ask about priority: Nakashima and Shestakov both did parallel work, and Shannon's paper does not cite them; Shannon's place is the complete, workable design calculus.

## Slide 16: Backup Q&A: Is the simplest circuit guaranteed? / What about timing and delay?
1
2
3
4
5
6
A
B
C
D
SHEET
16
PROJECT
Backup Sheets · Shannon 1937
DRAWN SAMPLE DATE 1937-08-10 NTS
Backup Q&A · B
Q
Is the simplest circuit guaranteed?
Within limits. Among series-parallel forms it always finds the simplest; with arbitrary connections, only “in some cases”. How far it goes “depends somewhat on the ingenuity of the designer”. Mechanical methods came in the 1950s: the Karnaugh map and Quine–McCluskey.
Source: thesis, Chapter I; AIEE paper, Sections I and IV (p.713, p.721).
Within series-parallel forms
Always finds the simplest
Any connections (e.g. bridges)
Simplest only in some cases
Doing the simplification
Relies on skill with theorems
Q
What about timing and delay?
Not just combinational circuits. Section III treats delayed relays: X(t − p) is a contact delayed by p seconds. Section IV adds a new variable per extra stage of operation, as in the Section V lock. A general method for sequential synthesis and state reduction came later, from Huffman in 1954.
Source: AIEE paper, Sections III (delay, p.718), IV (extra variables, p.721), V (lock); Huffman (1954).
X(t)
X(t − p)
p
High = 1 (open), low = 0 (closed); contact lags coil by p
← Back to sheet 8
← Back to contents
Notes: Backup sheet B. If asked whether the simplest circuit is guaranteed: yes for series-parallel circuits, only in some cases for general connections, and simplification takes skill; systematic algorithms came later with the Karnaugh map and Quine–McCluskey. If asked about timing: Section III handles delayed relays, Section IV gives the rule of one new variable per extra stage in a sequential system, with the Section V combination lock as the example, and the general theory came from Huffman in 1954.